# Huntland Water System Water Quality Report for 20221998

Is my drinking water safe?

Yes, our water meets all of EPA’s health standards. We have conducted numerous tests for over 80 contaminants that may be in drinking water.  As you’ll see in the chart on the back, we only detected 11 of these contaminants.  We found all of these contaminants at safe levels.

What is the source of my water?

Your water, which is ground water, comes from the Wells. Our goal is to protect our water from contaminants and we are working with the State to determine the vulnerability of our water source to potential contamination. The Tennessee Department of Environment and Conservation (TDEC) has prepared a Source Water Assessment Program (SWAP) Report for the untreated water sources serving water to this water system.  The SWAP Report assesses the susceptibility of untreated water sources to potential contamination.  To ensure safe drinking water, all public water systems treat and routinely test their water.  Water sources have been rated as reasonably susceptible, moderately susceptible or slightly susceptible based on geologic factors and human activities in the vicinity of the water source.  The Huntland Water System sources rated as reasonably susceptible to potential contamination.

An explanation of Tennessee’s Source Water Assessment Program, the Source Water Assessment summaries, susceptibility scorings and the overall TDEC report to EPA can be viewed online at https://www.tn.gov/environment/article/wr-wq-source-water-assessment or you may contact the Water System to obtain copies of specific assessments.

A wellhead protection plan is available for your review by contacting Jack Atchley at the Huntland Water System between 7:00 A.M. to 3:30 P.M. weekdays.

# Why are there contaminants in my water?

Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants.  The presence of contaminants does not necessarily indicate that water poses a health risk.  More information about contaminants and potential health effects can be obtained by calling the Environmental Protection Agency’s Safe Drinking Water Hotline (800-426-4791).

Este informe contiene información muy importante.  Tradúscalo o hable con alguien que lo entienda bien.

For more information about your drinking water, please call Jack Atchley at 1-931-469-5522.

# How can I get involved?

The Board of Mayor and Alderman meets on the third Tuesday  night at 6:30 PM at the community center .  Please feel  free to participate in these meetings.

Is our water system meeting other rules that govern our operations?

The State and EPA require us to test and report on our water on a regular basis to ensure its safety. We have met all of these requirements.  Results of unregulated contaminant analysis are available upon request.  We want you to know that we pay attention to all the rules.

# Other Information

The sources of drinking water (both tap water and bottled water) include rivers, lakes, streams, ponds, reservoirs, springs, and wells. As water travels over the surface of the land or through the ground, it dissolves naturally-occurring minerals and, in some cases, radioactive material, and can pick up substances resulting from the presence of animals or from human activity.

Contaminants that may be present in source water:

· Microbial contaminants, such as viruses and bacteria, which may come from sewage treatment plants, septic systems, agricultural livestock operations, and wildlife.

· Inorganic contaminants, such as salts and metals, which can be naturally-occurring or result from urban stormwater runoff, industrial, or domestic wastewater discharges, oil and gas production, mining, or farming.

· Pesticides and herbicides, which may come from a variety of sources such as agriculture, urban stormwater runoff, and residential uses.

· Organic chemical contaminants, including synthetic and volatile organic chemicals, which are by-products of industrial processes and petroleum production, and can also come from gas stations, urban stormwater runoff, and septic systems.

· Radioactive contaminants, which can be naturally-occurring or be the result of oil and gas production and mining activities.

In order to ensure that tap water is safe to drink, EPA and the Tennessee Department of Environment and Conservation prescribe regulations which limit the amount of certain contaminants in water provided by public water systems. FDA regulations establish limits for contaminants in bottled water which must provide the same protection for public health.

Cross Connection

We are required to have a cross connection and backflow prevention inspection program ongoing each year. Never submerge hoses in buckets, pools, tubs, or sinks. Always keep the end of the hose clear of possible contaminants. Never use spray attachments for poison or cleaning without a backflow prevention device. Buy and install inexpensive backflow prevention devices for threaded faucets around your house or business if you do this. When a water line breaks or the main is drained for repairs, backsiphonage and backflow can occur when the pressure drops causing bacteria or poisons to enter the water lines.

# Do I Need To Take Special Precautions?

Some people may be more vulnerable to contaminants in drinking water than the general population.  Immuno-compromised persons such as persons with cancer undergoing chemotherapy, persons who have under-gone organ transplants, people with HIV/AIDS or other immune system disorders, some elderly, and infants can be particularly at risk from infections. These people should seek advice about not only their drinking water, but food preparation, personal hygiene, and precautions in handling infants and pets from their health care providers. EPA/CDC guidelines on appropriate means to lessen the risk of infection by Cryptosporidium and other microbiological contaminants are available from the Safe Drinking Water Hotline (800-426-4791).

Lead in Drinking Water

If present, elevated levels of lead can cause serious health problems, especially for pregnant women and young children. Lead in drinking water is primarily from materials and components associated with service lines and home plumbing. Huntland Water System is responsible for providing high quality drinking water, but cannot control the variety of materials used in plumbing components. When your water has been sitting for several hours, you can minimize the potential for lead exposure by flushing your tap for 30 seconds to 2 minutes before using water for drinking or cooking. If you are concerned about lead in your water, you may wish to have your water tested. Information on lead in drinking water, testing methods, and steps you can take to minimize exposure is available from the Safe Drinking Water Hotline or at http://www.epa.gov/lead/protect-your-family%23water%23water

Water System Security

Following the events of September 2001, we realize that our customers are concerned about the security of their drinking water.  We urge the public to report any suspicious activities at any utility facilities, including treatment plants, tanks, fire hydrants, etc. to 931-636-2546.

Think before you flush!

Flushing unused or expired medicines can be harmful to your drinking water. Properly disposing of unused or expired medication helps protect you and the environment. Keep medications out of Tennessee's waterways by disposing in one of our permanent pharmaceutical take back bins. There are nearly 100 take back bins located across the state, to find a convenient location please visit: https://www.tn.gov/environment/article/sp-unwanted-pharmaceuticals

W  a  t  e  r     Q  u  a  l  i  t  y     D  a  t  a

What does this chart mean?

- MCLG -  Maximum Contaminant Level Goal, or the level of a contaminant in drinking water below which there is no known or expected risk to health.  MCLGs allow for a margin of safety.

- MCL - Maximum Contaminant Level, or the highest level of a contaminant that is allowed in drinking water. MCLs are set as close to the MCLGs as feasible using the best available treatment technology. To understand the possible health effects described for many regulated constituents, a person would have to drink 2 liters of water every day at the MCL level for a lifetime to have a one-in-a-million chance of having the described health effect.

- MRDL: Maximum Residual Disinfectant Level or MRDL: The highest level of a disinfectant allowed in drinking water. There is convincing evidence that addition of a disinfectant is necessary for the control of microbial contaminants.

- MRDLG: Maximum residual disinfectant level goal.  The level of a drinking water disinfectant below which there is no known or expected risk to health.  MRDLGs do not reflect the benefits of the use of disinfectants to control microbial contaminants.

- AL - Action Level, or the concentration of a contaminant which, when exceeded, triggers treatment or other requirements which a water system must follow.

- Below Detection Level (BDL) - laboratory analysis indicates that the contaminant is not present at a level that can be detected.

- Non-Detects (ND) - laboratory analysis indicates that the contaminant is not present.

- Parts per million (ppm) or Milligrams per liter (mg/l) – explained as a relation to time and money as one part per million corresponds to one minute in two years or a single penny in $10,000.

- Parts per billion (ppb) or Micrograms per liter - explained as a relation to time and money as one part per billion corresponds to one minute in 2,000 years, or a single penny in $10,000,000.

- Picocuries per liter (pCi/L) - picocuries per liter is a measure of the radioactivity in water.

- Millirems per year (mrem/yr) - measure of radiation absorbed by the body.

- Million Fibers per Liter (MFL) - million fibers per liter is a measure of the presence of asbestos fibers that are longer than 10 micrometers.

- Nephelometric Turbidity Unit (NTU) - nephelometric turbidity unit is a measure of the clarity of water. Turbidity in excess of 5 NTU is just noticeable to the average person.

- RTCR – Revised Total Coliform Rule.  This rule went into effect on April 1, 2016 and replaces the MCL for total coliform with a Treatment Technique Trigger for a system assessment.

- TT - Treatment Technique, or a required process intended to reduce the level of a contaminant in drinking water.

| Contaminant | Violation Yes/No | Level Found | Range of Detections | Date of Sample | Unit Measurement | MCLG | MCL | Likely Source of Contamination |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Total Coliform Bacteria | No | 0 |  | 2022 |  | 0 | <2 positive samples | Naturally present in the environment |
| Total Coliform Bacteria (RTCR) | No | 0 |  | 2022 |  | 0 | TT Trigger | Naturally present in the environment |
| Turbidity1 | No | .29 | .04-.29 | 2022 | NTU | N/A | TT | Soil runoff |
| Copper* | No | 90th%=0.129 |  | 8/2022 | ppm | 1.3 | AL=1.3 | Corrosion of household plumbing systems; erosion of natural deposits; leaching from wood preservatives |
| Lead* 4 | No | 90th%=.001 |  | 8/2022 | ppb | 0 | AL=15 | Corrosion of household plumbing systems, erosion of natural deposits |
| Nitrate- as Nitrogen 5 | No | 4.18 |  | 5/2022 | ppm | 10 | 10 | Runoff from fertilizer use; leaching from septic tanks, sewage; erosion of natural deposits |
| Sodium | No | 15.3 |  | 8/2022 | ppm | N/A | N/A | Erosion of natural deposits; used in water treatment |
| Atrazine | No | ND |  | 2022 | ppb | 3 | 3 | Runoff from herbicide used on row crops |
| TTHM6 [Total trihalomethanes] | No | 12.3 Ave. | 4.09-23.7 | 2022 | ppb | n/a | 80 | By-product of drinking water chlorination |
| Haloacetic Acids (HAA5) | No | 3.51 Ave. | ND- 7.96 | 2022 | ppb | N/A | 60 | By-product of drinking water disinfection. |
| Total Organic Carbon2 | No | BDL |  | 2022 | ppm | TT | TT | Naturally present in the environment. |

| Chlorine | No | 1.8 Ave. | 0.6-2.3 | 2022 | ppm | 4 | 4 | Water additive used to control microbes. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

*During the most recent round of Lead and Copper testing, 0 out of 10 households sampled contained concentrations exceeding the action level.

1100% of our samples were below the turbidity limit.

2We have met all treatment technique requirements for Total Organic Carbon removal.

3   IRON:  Iron occurs naturally in our raw water and occasionally accumulates in the distribution system. Iron shows up as “red” water or “rusty” water at your tap.    Although you do not want to drink water that is not clear, iron is not considered to be a hazard to your health. We test for iron daily and our finish water is usually .01 ppm or less. The aesthetic limit for iron is 0.30 ppm.

4 LEAD: Infants and young children are more vulnerable to lead in drinking water than the general population. It is possible that lead levels in your home may be higher than at other homes in the community as a result of materials used in your home’s plumbing. If you are concerned about elevated lead levels in your home’s water, you may wish to have your water tested and you may want to flush your tap for 30 seconds to 2 minutes before using tap water. Additional information is available from the Safe Drinking Water Hotline (1-800-426-4791).

5 Nitrate: Nitrate in drinking water at levels above 10 ppm is a health risk for infants of less than 6 months of age.      High nitrate levels in drinking water can cause blue baby syndrome. Nitrate levels may rise quickly for short period of time because of rainfall or agricultural activity. If you are caring for an infant you should ask advice from your health provider. Results for Huntland  were well below the 10 ppm limit. Huntland water tested at 4.38 ppm

6 While your drinking water meets EPA’s standard for trihalomethanes, it does contain low levels. Some people who drink water containing trihalomethanes in excess of the MCL over many years may experience problems with their liver, kidneys, or central nervous system, and may have an increased risk of getting cancer.

NOTICE OF VIOLATION

IMPORTANT   INFORMATION  ABOUT YOUR DRINKING WATER

“ Monitoring requirements not met for the Huntland Water System”

Our water system violated drinking water requirements over the past year. Even though these were not emergencies, as our customers, you have the right to know what happened and what we are doing(did) to correct the situations.

“ We are required to monitor your drinking water for specific contaminants on a regular basis. Results of regular monitoring are an indicator of whether or not our drinking water meets health standardsa. During the 2nd quarter of 2022 we did not monitor or test for Atrazine and therefore cannot be sure of the quality of your drinking water during that time. We did test for atrazine on July 26th, 2022 and the results indicated no atrazine in our water.

- Atrazine is a herbicide and plan growth regulator used primarily on corn and soybeans.                            It is slightly soluble in water and is regulated by the Environmental Protection Agency.

What should you do ?

There is nothing you need to do at this time.

Listed below is the lists of contaminant(s) we did not properly test for during last year, how often we are supposed to sample for this contaminant, how many samples we were supposed to take, how many samples we took, when samples should have been taken, and the date on which follow-up samples were taken.

Contaminant – Atrazine  - required 1 sample each year in the 2nd quarter( April, May or June, 2022)       Sample was taken late on July 26, 2022 and no Atrazine was detected.

What is being done?

We have contacted our lab who supplies the sampling kits and have prepared a check-list.

For more information: Contact Jack Atchley at 1-931-469-5522 or Town Hall at 100 Banks Street.

**Please share this information with all the people who drink this water, especially those who may not have received this notice directly (for example, people in apartments, nursing homes, schools, and businesses). This notice can be posted in public places. This notice is being place at the Community Center, the Post Office and at the Water Department main office and can be posted in other public places and copies can be distributed to those people as well.

This notice is being sent to you by the Huntland Water System ID# TN0000317